## Slide 1: NatHERS Whole of Home Technical
Presenter(s): Michael Young
Date: 22 August 2023
DCCEEW.gov.au

## Slide 2
Source: Barramundi, Aboriginal x-ray art. Photo: Jon Connell. Creative Commons BY 2.0 (cropped)

## Slide 3: Scope
In this webinar we will cover:
Overview of Whole of Home
Undertaking a Whole of Home Assessment
Heating and Cooling Appliances
Hot Water
Lighting
Pools and Spas
On-Site Renewable Energy
On-Site Energy Storage
Plug Loads and Cooking Loads
Questions

## Slide 4: Disclaimer
This webinar DOES NOT cover any software or tool. Please speak with software developers to learn about the timings for the release of their Whole of Home product and for training in the use of that tool.
A Demo of the Benchmark tool is available: https://www.nathers.gov.au/WholeofHome/software-development
This webinar assumes that you have completed either the Overview webinar or have a basic understanding of Whole of Home.

## Slide 5: Overview of NatHERS Whole of Home

## Slide 8: Undertaking a Whole of Home Assessment

## Slide 9: NatHERS Assessment?
The NatHERS Whole of Home assessment builds on the existing NatHERS thermal assessment that is used to verify compliance with the energy efficiency performance requirements of the NCC.
From 1 October 2023, there will be two energy efficiency performance requirements for residential buildings under the NCC:
  the thermal performance -> Thermal Assessment
  the energy usage performance -> Whole of Home performance rating

## Slide 10: NCC 2022 Transition arrangements
1 May 2023 - 30 September 2023

## Slide 11: NCC 2022 Transition arrangements
State and territory variations may apply where jurisdictions require Assessors to use specific versions of the NCC

## Slide 12: NCC 2022 Transition arrangements
Assessment meeting the NSW BASIX thermal performance standards must continue to use v3.21 software until 30 September 2023

## Slide 13: Compliance with NCC 2019
If you choose to comply with NCC 2019, you must use:
Chenath
Engine
v3.21
Thermal only NatHERS
certificate
Technical Note June 2019
ABCB Standard 2019.1
load limits
Subclause 3.12.0(a)(i) NCC 2019 Volume 2
Clause J0.2
NCC 2019
Volume 1

## Slide 14: Compliance with NCC 2022
If you choose to comply with NCC 2022, you must use:
Chenath
Engine
v3.22*
NatHERS
Certificate with WoH
Technical Note Sep 2022
ABCB Standard 2022.1
load limits
Specif. 42 NCC 2022 Volume 2
Section J2D2
NCC 2022
Volume 1
*When available

## Slide 15: From 1 October 2023 onwards
Chenath
Engine
v3.21 not compliant
Chenath
Engine
v3.21 via request
Chenath
Engine
v3.22 only
NatHERS
Certificate with WoH

## Slide 17: Who can undertake a WoH assessment?
Non-accredited Assessor
Undertake WoH tool training
Complete this WoH Technical webinar
Complete the WoH Technical quiz
Accredited WoH Assessor
Undertake WoH tool training
Complete this WoH Technical webinar
Complete the WoH Technical quiz
Provide certificate to your AAO

## Slide 18: Example

## Slide 19: Case study
NatHERS Example 4 drawing set https://www.nathers.gov.au/sites/default/files/2022-12/NatHERS%20Example4_drawings.pdf

## Slide 20: Heating and Cooling Appliances

## Slide 21: Heating appliances
Wood heater
Ducted
heat pump
air-conditioner
Electric resistive heater
Ducted
gas heater
The Whole of Home assessment tools will allow selection from the following heating appliances:
Non-ducted
gas heater
(space heater)
Non-ducted
heat pump
air-conditioner
Correct sizing for the dwelling is very important

## Slide 22: Cooling appliances
Ducted
air-conditioner
Evaporative
cooler
The Whole of Home assessment tools will allow selection from the following cooling appliances:
Non-ducted
air-conditioner
No delineation between reverse cycle and cooling-only air-conditioners

## Slide 23: Key concepts
Same 69 NatHERS Climate Zones
Cold
Hot and Humid
Mixed

## Slide 24: Technical Note requirements

## Slide 25: Technical Note requirements

## Slide 26: Technical Note requirements

## Slide 27: Technical Note requirements

## Slide 28: Data required for the WoH assessment
How zone is heated and cooled
Details of appliance
Climate type (zone)
Energy usage
Star rating

## Slide 35
assessment..
Heating and cooling appliance case study

## Slide 36: Hot Water

## Slide 37: Key concepts
Solid fuel
Off-peak electric
PV Diverters
Solar thermal
(electric boosted)
Gas
instantaneous
Solar thermal
(gas boosted)
Heat pump
Instantaneous
electric
Gas storage
Types of water heaters
Continuous
electric

## Slide 38: Key concepts
Small-scale Technology Certificates (STC)
Equal to 1 megawatt hour of renewable electricity either generated or displaced by eligible small-scale renewable energy systems such as solar PV, wind and hydro and solar water heaters and air source heat pumps

## Slide 39: Technical Note requirements

## Slide 40: Technical Note requirements

## Slide 41: Technical Note requirements

## Slide 42: Technical Note requirements

## Slide 44: Technical Note requirements

## Slide 45: Technical Note requirements

## Slide 48: Data required for the WoH assessment
Hot water system specified
Type of diverter system if PV diverter
STC value

## Slide 51: Hot water case study
Must use
Electric
storage
hot water
off-peak
No water heating system specified
Default values must be used
No gas outlet or appliance
specified

## Slide 52: Lighting

## Slide 53: Key concepts
Lighting power density represents the load of lighting equipment in a specified area. Typically represented as Watts per square metre (W/m2).
CFL
CFL
LED
Linear and
Circular
fluorescent
Halogen
Halogen
Source: https://www.yourhome.gov.au/energy/lighting

## Slide 54: Technical Note requirements

## Slide 55: Data required for the WoH assessment
Lighting power density (in W/m2)

## Slide 56: Lighting case study

## Slide 57: Pools and Spas

## Slide 58: Key concepts
Pool
cleaning
system type
Pool volume
(m3)
Pool
surface area
(m2)
Pool
pump type

## Slide 59: Technical Note requirements

## Slide 60: Technical Note requirements

## Slide 61: Technical Note requirements

## Slide 62: Data required for the WoH assessment
Water
cleaning
system type
Pool or spa
volume or
surface area
Pump
Star rating
(2019 GEMS)
Pool or spa
pump type

## Slide 63: Pool and spa case study
No pool or spa is specified

## Slide 66: On-Site Renewable Energy

## Slide 67: Key concepts
PV system size
(kW)
Panel
direction
(orientation)
Inverter
capacity
of arrays or
strings
Panel
inclination
(angle)

## Slide 68: Technical Note requirements

## Slide 69: Technical Note requirements

## Slide 72: Technical Note requirements

## Slide 73: Data required for WoH assessment
PV system size
(kW)
Panel
direction
(orientation)
Inverter
capacity
of arrays or
strings
Panel
inclination
(angle)

## Slide 74
No renewable energy generation is specified
On-Site Renewable Energy case study

## Slide 77: On-Site Energy Storage

## Slide 78: Key concepts
Battery types
Lithium-ion
Lead acid
Zinc bromine

## Slide 79: Technical Note requirements

## Slide 80: Data required for WoH assessment
Battery type
Battery size

## Slide 81
No battery is specified
On-Site Energy Storage case study

## Slide 82: Plug Load and Cooking Loads

## Slide 83: Key concepts
Plug load
Cooking load

## Slide 85: Technical Note requirements

## Slide 86: Data required for WoH assessment
Electric cooktop
Electric oven
Gas cooktop
Induction cooktop
Energy sources for cooking appliances

## Slide 87
assessment..
Plug Load and Cooking Loads case study

## Slide 90: Example – Melbourne

## Slide 91: Example – Brisbane

## Slide 92: Example – Canberra

## Slide 93
In this webinar we have covered:
Overview of Whole of Home
Undertaking a Whole of Home Assessment
Heating and Cooling Appliances
Hot Water
Lighting
Pools and Spas
On-Site Renewable Energy
On-Site Energy Storage
Plug Loads and Cooking Loads
Summary

## Slide 94: Questions?

## Slide 95
Access and complete the quiz at:
https://transformed-pty-ltd-short-courses.thinkific.com/courses/nathers-whole-of-home-technical
You will need to register
Complete the Quiz